## Slide 1: : Domain-Specific Accelerator Generator Hardware Perspective
Sihao Liu
PolyArch Research Group
University of California, Los Angeles
Oct 2nd, 2022; MICRO 2022 Tutorial
(2:30 PM – 4:15 PM)

## Slide 2: Outline
Micro-architecture Overview (30 min)
  Stream Dispatcher
  Spatial Memory System & Sync. System
  Spatial Compute System
Coffee Break (30 min)
Hand-on: Compose Your Own DSA (30 min)
  Architecture Description Graph (ADG)
  Using our own DSA by using Domain-specific Language
Hard-on: RTL & FPGA Simulation (15 min)
  How to do RTL simulation with customized ISA
  Understand the simulation log and FPGA Flow

## Slide 3: Before we start: Code Structure Overview
ChipYard
SoC integration, RTL sim, FPGA
DSAGEN2
Implementation of DSA , Overlay, Test
Path: dsa-framework/chipyard
Path: dsa-framework/chipyard/generators/dsagen2

## Slide 4: Before we start: DSAGEN Code Structure
source code
components
Four major components:
comp: spatial computing system, CGRA
ctrl: stream management
mem: memory system, DMA, Scratchpad, etc.
sync: vector ports, data synchronization
Common structure:
bundle: IO interface definition
config: reconfiguration part, the “Chisel” part
diplomacy: parameter handshake for arbitrary topology
impl: hardware implementation, the “Verilog” part
module: connect “Chisel” and “Verilog” part
Note: The whole project is written in Chisel (Scala)
“Chisel”: flexible, parameterizable part of design
“Verilog”: static, fixed part of design
Path: dsa-framework/chipyard/
generators/dsagen2

## Slide 5: Outline
Micro-architecture Overview (30 min)
  Stream Dispatcher
  Spatial Memory System & Sync. System
  Spatial Compute System
Coffee Break (30 min)
Hand-on: Compose Your Own DSA (30 min)
  Architecture Description Graph (ADG)
  Using our own DSA by using Domain-specific Language
Hard-on: RTL & FPGA Simulation (15 min)
  How to do RTL simulation with customized ISA
  Understand the simulation log and FPGA Flow
Notes: Here is an outline of this section. We first look at the high-level programming interface.

## Slide 6: DSAGEN Architecture Overview
Integrate as RoCC accelerator
DCache (HellaCache) for bitstream load
L2 Cache access via NoC
Multi-core support
FPGA proved
Four major subsystem:
Spatial Compute System – CGRA Generator
Spatial Memory System – Memory Gen.
Synchronization System – Vector ports
Control System – Manage Streams

## Slide 7: Control System: Stream Dispatcher
Source Code Path
chipyard/generators/dsagen2/src/main/scala/dsagen2/
ctrl/module
RoCC interface entrance
Dcache (HellaCache) for bitstream load
Stream Command Decode
A simple out-of-order issue queue
Support barrier command
Notes: Need to motivate people
The purpose of stream dispatcher, what does this unit do, stream command coordination
talking about the stream disp function
What id the design requirement
Issue command quickly back to back,
Quickly close timing what is the round-trip time
How does the micro-arch
Another interface for RoCC
Big purpose: get people motivated, show the purple of each component, explain why it is interesting why and why not.
Why RoCC, how does RoCC work; what is the benefit of design like that
What is the unit? What is the design requirement? What is our motivation? What the design is? XYZ?

## Slide 8: Stream Dispatcher: Why we need it?
A bridge between RISC-V and DSA
Manage the stream pattern parameters
Manage stream dependency & resources
Solve stream conflicts – Out-of-order issue
Config Stream
Start
Stream
Control
Stream

## Slide 9: Stream Concurrent Execution Model
for (int j = 0; i < M; ++j)
for (int i = 0; i < N; ++i)
c[j*K+i] += a[j*K+i] * b[j*K+i];
×
＋
a[0:N]
c[0:N]
Streams
Dataflow
c[N+1:2N]
a[N+1:2N]
b[0:N]
b[N+1:2N]
c[0:N]
c[N+1:2N]
Memory
Output port
Input port
×
＋
Control Core
a[N+1:2N]
b[N+1:2N]
c[N+1:2N]
a[0:N]
b[0:N]
c[0:N]
Concurrent
(Out-of-Order)
Sequential
Notes: Point the problem of execution mode, and introduce the hardware to solve that

## Slide 10: Stream Dispatcher: What does it do?
SS-Inst
Stream-Specialized Instruction (SS-Inst) arrived
  SS-Inst goes buffered in command FIFO
  Each SS-Inst can update up to two parameters in Reg. File
  Config to special registers will trigger bitstream reload

## Slide 11: Stream Dispatcher: What does it do?
SS-Inst
Stream-Specialized Instruction (SS-Inst) arrived
  SS-Inst goes buffered in command FIFO
  Each SS-Inst can update up to two parameters in Reg. File
  Config to special registers will trigger bitstream reload
SS-Inst can trigger stream instantiation
  Parameter values read out from register file
  Decode stage forms stream entry with elaborated param.
  Elaborated stream entry sent to stream dispatcher queue
addr, 1d/2d, len, etc.
stream entry

## Slide 12: Stream Dispatcher: What does it do?
SS-Inst
Stream-Specialized Instruction (SS-Inst) arrived
  SS-Inst goes buffered in command FIFO
  Each SS-Inst can update up to two parameters in Reg. File
  Config to special registers will trigger bitstream reload
SS-Inst can trigger stream instantiation
  Parameter values read out from register file
  Decode stage forms stream entry with elaborated param.
  Elaborated stream entry sent to stream dispatcher queue
  Barrier entry can also be formed and put into Queue
Dispatch queue checks idle/busy of scoreboard
  If the target stream engines (explained later) busy?
  If the target ports busy?
addr, 1d/2d, len, etc.
stream entry
barrier
Busy/Idle?
Busy/Idle
?

## Slide 13: Stream Dispatcher: What does it do?
SS-Inst
Stream-Specialized Instruction (SS-Inst) arrived
  SS-Inst goes buffered in command FIFO
  Each SS-Inst can update up to two parameters in Reg. File
  Config to special registers will trigger bitstream reload
SS-Inst can trigger stream instantiation
  Parameter values read out from register file
  Decode stage forms stream entry with elaborated param.
  Elaborated stream entry sent to stream dispatcher queue
  Barrier entry can also be formed and put into Queue
Dispatch queue checks idle/busy of scoreboard
  If the target stream engines (explained later) busy?
  If the target ports busy?
  Dispatched to target stream engine
addr, 1d/2d, len, etc.
stream entry
barrier
Busy/Idle?
Busy/Idle
?

## Slide 14: Memory System: Design Requirement? Why?
DMA
Main Memory
DRAM (~GB)
Scratchpad
Memory
(~KB)
Scratchpad
Memory
Recurrence
Bus
Recurrence Engine
Stream
Generation
Generate Engine
Scalar (Reg)
Retrieve
Register Engine
Design requirement
  We want to keep hardware simple – A shared-module design methodology
  We want it to have high-performance – A fully-pipelined design
  We want it to be physical design friendly – Conservative timing, blocked memory
Notes: Load and Store data
What is the requirement
Multiple stream
Arbitrate stream
Need to be fully pipeline and full saturate the hardware
Critical path and timing issue
Different kinds of memory nodes
Keep the hardware simple, modularity
Share the pipeline
Why we have common data path

## Slide 15: Memory System: Why we need it?
Convert to actual data stream.
Decide which takes resource
Address generation based on
Report stream engine busy/idle to Stream Dispatcher
stream entry
stream entry
stream entry
Stream
Issue
Stream
Request
Stream
Generation
Source Code Path
$SSchipyard/generators/dsagen2/src/main/scala/dsagen2/
mem/module
agent DMA Only, TileLink Requestor/Receiver
agu Stream Request stage
bank Scratchpad Bank (FPGA BRAM optimized)
bus Broadcast stream response to all In Ports
ngu Generate Engine only, affine sequence
rob DMA Only, re-order memory response
stab Stream Table of Stream Issue stage
tlb DMA Only, address translation
xbar solve Scratchpad Bank conflict
Code Organization

## Slide 16: Memory System: What does it do?
Stream
Issue
Stream
Request
Stream
Generation
read stream 1
Stream Entries are dispatched to Stream Table
  Each stream entry relates to a certain port
  Read streams and write streams are mixed
read stream 2
write stream 1

## Slide 17: Memory System: What does it do?
Stream
Issue
Stream
Request
Stream
Generation
read stream 1
Stream Entries are dispatched to Stream Table
  Each stream entry relates to a certain port
  Read streams and write streams are mixed
Stream Entries are issued to Stream Request
  A simple round-robin style is enough for most case*
read stream 2
write stream 1

## Slide 18: Memory System: What does it do?
Stream
Issue
Stream
Request
Stream
Generation
Stream Entries are dispatched to Stream Table
  Each stream entry relates to a certain port
  Read streams and write streams are mixed
Stream Entries are issued to Stream Request
  A simple round-robin style is enough for most case*
  Optimization can be applied here – One-hot bypass
read stream 2
write stream 1
read stream 1

## Slide 19: Memory System: What does it do?
Stream
Issue
Stream
Request
Stream
Generation
Stream Entries are dispatched to Stream Table
  Each stream entry relates to a certain port
  Read streams and write streams are mixed
Stream Entries are issued to Stream Request
  A simple round-robin style is enough*
  Optimization can be applied here – One-hot bypass
  Elaborated stream entry converted to address and bitmask
read stream 2
write stream 1
read stream 1
addr, bitmask: [00111111]

## Slide 20: Memory System: What does it do?
Stream
Issue
Stream
Request
Stream
Generation
Stream Entries are dispatched to Stream Table
  Each stream entry relates to a certain port
  Read streams and write streams are mixed
Stream Entries are issued to Stream Request
  A simple round-robin style is enough*
  Optimization can be applied here – One-hot bypass
  Elaborated stream entry converted to address and bitmask
Stream Generation uses address and bitmask for memory
  Read data from main memory / scratchpad bank / generate ...
read stream 2
write stream 1
read stream 1
addr, bitmask: [00111111]
data: [--, BB, XX, YY]

## Slide 21: Memory System: What does it do?
Stream
Issue
Stream
Request
Stream
Generation
Stream Entries are dispatched to Stream Table
  Each stream entry relates to a certain port
  Read streams and write streams are mixed
Stream Entries are issued to Stream Request
  A simple round-robin style is enough*
  Optimization can be applied here – One-hot bypass
  Elaborated stream entry converted to address and bitmask
Stream Generation uses address and bitmask for memory
  Read data from main memory / scratchpad bank / generate ...
  Write data to main memory / scratchpad bank / recurrence
read stream 2
write stream 1
read stream 1
addr, bitmask: [00111111]
data: [--, BB, XX, YY]

## Slide 22: Memory System: What does it do?
Stream
Issue
Stream
Request
Stream
Generation
Stream Entries are dispatched to Stream Table
  Each stream entry relates to a certain port
  Read streams and write streams are mixed
Stream Entries are issued to Stream Request
  A simple round-robin style is enough*
  Optimization can be applied here – One-hot bypass
  Elaborated stream entry converted to address and bitmask
Stream Generation uses address and bitmask for memory
  Read data from main memory / scratchpad bank / generate /...
  Write data to main memory / scratchpad bank / recurrence /...
Stream Response (for read stream only)
  Send data (broadcast) to all In Ports
read stream 2
write stream 1
read stream 1
addr, bitmask: [00111111]
data: [--, BB, XX, YY]

## Slide 23: Vector Ports: What? Why?
read stream 1
addr, bitmask: [00111111]
data: [--, BB, XX, YY]
A synchronization interface between mem. and comp.
A crossbar (for data alignment) + memory banks (storage)
Main
Memory
Scratch
pad
1
Scratch
pad
2
Spatial Memory System
Vector Port
Bank
Bank
Spatial
Compute
System
Notes: Basic implementation and Stream State and Port Repeat

## Slide 24: Vector Ports: What? Why?
read stream 1
addr, bitmask: [00111111]
data: [--, BB, XX, YY]
A synchronization interface between mem. and comp.
A crossbar (for data alignment) + memory banks (storage)
A small finite state machine
  Broadcast (duplicate) stream
  Repeat previous stream response
  Padding the response to make it multiple of vector length
Main
Memory
Scratch
pad
1
Scratch
pad
2
Spatial Memory System
Vector Port
Bank
Bank
Spatial
Compute
System
+
b [...] = a[...] + a [...]
VP 1
VP 2
a[...]
VP
[1, 3, 5, 7, 9, 11, 13]
[1, 3, 5, 7, 9, 11, 13]
[1, 3, 5, 7, 9, 11, 13]
[1, 3, 5, 7, 9]
[1, 3, 5, 7, 9]
[1, 3, 5]
x3
x2
x1
VP
[1, 3, 5, 7 ]
[9, 11, 13, --]
[3, 5, 7, 9]
[11, 13,17, -- ]
[1, 3, 5, 7, 9, 11, 13 ]
[3, 5, 7, 9, 11, 13, 17]
Linear 2D stream:
Vector x 4
Notes: The to

## Slide 25: Spatial Computing System – DSA-CGRA-GEN
A 4-Input 3-Output Switch
Function
Unit
Instruction Buffer
Instruction Scheduler
Register
File
MUX
MUX
A 2-input 1-Output Processing Element (PE)
Processing Element (PE)
Switch (SW)
Check our old tutorial for details

## Slide 26: Before Coffee Break: Hand-on Exercise
Build a Demo DSA and Compile to RTL Simulation File
Compile to Verilator/VCS Simulation File
$ cd $SS/chipyard
$ make -C sims/verilator CONFIG=DemoDSARocketConfig

## Slide 27: Before Coffee Break: Hand-on Exercise
Build a 7x5 Mesh CGRA and Compile to RTL Simulation File
Compile to Verilator Simulation File
$ cd $SS/chipyard
$ make -C sims/verilator CONFIG=MeshDSARocketConfig

## Slide 28: Coffee Break (3:00 ~ 3:30pm)
Notes: Thing:
Nowhere in the ports, core port serialization. Stream is design to be concurrent and the only place it is serialized is stream to the same port
Hard to understand the stream dispatcher, need a slide to include the stream concurrent execution model

## Slide 29: Outline
Micro-architecture Overview (30 min)
  Stream Dispatcher
  Spatial Memory System & Sync. System
  Spatial Compute System
Coffee Break (30 min)
Hand-on: Compose Your Own DSA (30 min)
  Architecture Description Graph (ADG)
  Using our own DSA by using Domain-specific Language
Hard-on: RTL & FPGA Simulation (15 min)
  How to do RTL simulation with customized ISA
  Understand the simulation log and FPGA Flow
Notes: Here is an outline of this section. We first look at the high-level programming interface.

## Slide 30: Architecture Description Graph (ADG)
Two ways to describe Domain-specific Accelerator (DSA)
  A machine-friendly format (JSON) that records parameters + topology of DSA
  A human-understandable format (Scala) that used for manual design
A JSON-list for DSA Nodes: Param.
A JSON-list for DSA Edges: Topology
Example Path
$SS/chipyard/generators/dsagen2/adg/Mesh2x2-Simple64-I2O2.json
Notes: two representation of the ADG,
Scala and JSON and brief

## Slide 31: Compute System: An CGRA Generator
val vport_i1 = createIVP(new FullIVPConfig)
val vport_i2 = createIVP(new FullIVPConfig)
val vport_o1 = createOVP(new FullOVPConfig)
val vport_o2 = createOVP(new FullOVPConfig)
vport_o1
vport_i2
vport_i1
val pe = createCompNode(new PE_Simple_Config)
val sw1 = createCompNode(new DefaultSWConfig)
val sw2 = createCompNode(new DefaultSWConfig)
val sw3 = createCompNode(new DefaultSWConfig)
val sw4 = createCompNode(new DefaultSWConfig)
sw1
sw2
sw3
sw4
pe
vport_o2

## Slide 32: A Scala Embedded DSL – Build A Simple CGRA
vport_o1
vport_i2
vport_i1
sw1
sw2
sw3
sw4
pe
// define connection vport_i1 --> sw1; vport_i1 --> sw2 vport_i2 --> sw1; vport_i2 --> sw2
sw3 --> vport_o1; sw3 --> vport_o2 sw4 --> vport_o1; sw4 --> vport_o2
sw1 <-> sw2 sw1 <-> sw3 sw2 <-> sw4 sw3 <-> sw4
sw1 --> pe sw2 --> pe sw3 --> pe sw4 <-> pe
vport_o2

## Slide 33: A Scala Embedded DSL – Adding Memory System
// adding memory val dma0 = createMemNode(new DefaultDMAConfig)
// connecting memory to VPs
dma0 --> vport_i1
dma0 --> vport_i2
vport_o1 --> dma0
vport_o2 --> dma0
// Finalized stage
autoConfigure()
tlNode := getMemAggTLNode
override val nPTWPorts: Int = numDMA
vport_o1
vport_i2
vport_i1
sw1
sw2
sw3
sw4
pe
vport_o2
DMA

## Slide 34: A Scala Embedded DSL – Build A Simple CGRA
vport_o1
vport_i2
vport_i1
sw1
sw2
sw3
sw4
pe
vport_o2
DMA
Example Path
$SS/chipyard/generators/dsagen2/
src/main/scala/dsagen2/top/example
Notes: path to the example files

## Slide 35: Hand-on Exercise (30 min)
Build a Demo DSA and Compile to RTL Simulation File
Compile to Verilator/VCS Simulation File
$ cd $SS/chipyard
$ make -C sims/verilator CONFIG=DemoDSARocketConfig

## Slide 36: Hand-on Exercise (30 min)
Build a 7x5 Mesh CGRA and Compile to RTL Simulation File
Compile to Verilator Simulation File
$ cd $SS/chipyard
$ make -C sims/verilator CONFIG=MeshDSARocketConfig

## Slide 37: Outline
Micro-architecture Overview (30 min)
  Stream Dispatcher
  Spatial Memory System & Sync. System
  Spatial Compute System
Coffee Break (30 min)
Hand-on: Compose Your Own DSA (30 min)
  Architecture Description Graph (ADG)
  Using our own DSA by using Domain-specific Language
Hard-on: RTL & FPGA Simulation (15 min)
  How to do RTL simulation with customized ISA
  Understand the simulation log and FPGA Flow
Notes: Here is an outline of this section. We first look at the high-level programming interface.

## Slide 38: Unit Test DSAGEN generated accelerator
Compile all test binaries
$ cd $SS/chipyard/generators/dsagen2
$ make ADG=<The ADG we just built.json> compile-microbench
$ cd adg
$ python3 $SS/scripts/sched_visualization.py Mesh7x5-Full64-Full7I5O.json
Run all unit tests
$ cd $SS/chipyard
$ make -C sims/verilator CONFIG=MeshDSARocketConfig ss-run

## Slide 39: Unit Test DSAGEN generated accelerator
Compile all test binaries
$ cd $SS/chipyard/generators/dsagen2
$ make ADG=<The ADG we just built.json> compile-microbench
$ cd adg
$ python3 $SS/scripts/sched_visualization.py Mesh7x5-Full64-Full7I5O.json
Run all unit tests
$ cd $SS/chipyard
$ make -C sims/verilator CONFIG=MeshDSARocketConfig ss-run
DMA
Scratchpad
Input Ports
Output Ports
CGRA

## Slide 40: RTL Simulation for real workloads
Simulate with RISC-V binaries (mv, crs) from previous session
  $ make -C sims/verilator CONFIG=MeshDSARocketConfig BINARY=$SS/dsa-apps/demo/ss-mv.riscv run-binary-fast
  $ make -C sims/verilator CONFIG=MeshDSARocketConfig BINARY=$SS/dsa-apps/demo/ss-crs.riscv run-binary-fast

## Slide 41: Understand Simulation Log
> chipyard/sims/[vcs/verilator]/output/ MeshDSARocketConfig /*.log
Accelerator part finished
Computation is correct
csv, [CPU #cycle], [1st DSA #cycle], [2nd DSA #cycle]

## Slide 42: Understand Simulation Log
> chipyard/sims/[vcs/verilator]/output/ MeshDSARocketConfig /*.log
A #cycle breakdown
  # configuration cycle
  # idle cycle
  # busy cycle
  ...
Full statistic header
  dsa-apps/compiled/Common/timing.h
Turn on debug mode
  `export DEBUG=1`

## Slide 43: FPGA Overlay Overview
C/C++
Kernels
(pragmas)
LLVM +
Dataflow Compiler
Compiled
RISCV+Accel
Binaries
Compile
RTL Generation
Design-space
Exploration
Runs on
Rec Bus
Memory
Ctrl.
＋
＋
＋
b[0:n
c[0:n]
a[0:n]
＋
RISCV CPU
Chisel-based
Hardware Generator
Arch. Desc. Graph
(ADG)
4-Core FPGA Overlay@ 92.7MHz
FPGA
RISCV CPU
RISCV CPU
Acce.
Acce.
Network-on-Chip
LLC
DRAM
Peripherals
SoC Integration by ChipYard
Physical Design
Notes: If i want to target FPGA, what should we do

## Slide 44: FPGA Overlay Limitation
This is NOT magic! mostly engineering effort.
Heavily depends on FPGA IP generator!
Integration is mostly done by ChipYard
  Need to generate Vivado FPGA IP
  FPGA Overlay is done by Chisel BlackBox Wrapper

## Slide 45: Hand-on: FPGA Flow Command
Compile FPGA bitstream
$ cd $SS/chipyard/fpga
$ make CONFIG=MeshDSARocketVCU118Config100MHz SUB_PROJECT=vcu118 bitstream
FPGA Bring-up Flow
// Where to fine the FPGA Bitstream
$ cd $SS/chipyard/fpga/generated-src/<Your CONFIG>/obj/VCU118FPGATestHarness.bit